## Slide 1
UNDERGRADUATE CAPSTONE PROJECT · SCHOOL OF ENGINEERING
EVSU SecureTap
NFC And Facial Recognition-Based Campus
Entry Monitoring System
Presented by
Zhander Jake Bastes Philip Lenard Peneda Mark William Brua
Panel : Cabral · Badilla · Alberca Adviser : Neil M. Pascual
August 2026

## Slide 2
OVERVIEW
Presentation Outline
AGENDA
02
01
Introduction & Background
02
Statement of the Problem
03
Objectives of the Study
04
Scope & Limitations
05
System Architecture
06
Core Innovation — Face Recognition
07
Core Innovation — Anti-Spoofing / Liveness
08
Core Innovation — Face + NFC Verification
09
Admin Dashboard & Reporting
10
Data Privacy & Security
11
Actual Accomplishments
12
Future Work & Conclusion

## Slide 3
INTRODUCTION
Why Gate Security Needs to Evolve
BACKGROUND
03
University gates are still largely secured the way they were decades ago — a guard checking a printed card by eye.
Cards prove possession,
not identity
A lost, borrowed, or forged ID goes unchecked.
Manual checks
don't scale
Guards fatigue during rush hours; verification quality drops.
RFID/NFC readers verify the card,
not the person
A tap only confirms a chip's ID, not who is holding it.
EVSU SecureTap combines continuous face recognition, a passive anti-spoofing layer, and an NFC card as a smart tiebreaker — verifying identity, not just an ID card.

## Slide 4
THE PROBLEM
Statement of the Problem
BACKGROUND
04
Lack of identity verification beyond physical identification credentials
Identification cards alone do not verify that the person presenting them is the rightful owner.
Face recognition alone is exploitable
A camera-only system with no liveness check can be fooled by a printed photo or a phone/tablet screen held up to the lens.
Manual verification is inconsistent
Guard-only checks vary with fatigue, shift changes, and traffic volume, especially during peak entry/exit periods.
Off-the-shelf hardware constraint
A real deployment can't assume depth or infrared sensors, the system must perform authentication effectively using affordable, readily
available hardware.

## Slide 5
GOALS
Objectives of the Study
OBJECTIVES
05
General Objective
To design and develop an integrated face-recognition and NFC-based gate entry/exit system for EVSU, with built-in anti-spoofing protection.
Specific Objectives
1
Implement facial recognition using ArcFace embeddings for gate scanning.
2
Integrate NFC authentication and automated tap-in/tap-out recording for students and staff.
3
Enable real-time monitoring and report generation for security personnel and administrators..
4
Build a role-based admin dashboard for live monitoring, user enrollment, and reporting.
5
Evaluate the system in terms of functionality, usability, reliability, and performance.

## Slide 6
BOUNDARIES
Scope & Limitations
OBJECTIVES
06
IN SCOPE
Continuous face-scan entry/exit logging per gate
NFC tap + manual ID fallback verification
Passive liveness detection against print & screen attacks
Student/staff enrollment with guided photo capture
Live monitoring, logs, and reporting dashboard
OUT OF SCOPE / LIMITATIONS
No defense against 3D/silicone masks (2D webcam only)
Guard-attended design, not an unattended kiosk
One camera & fixed direction per gate device
Matching thresholds are pre-deployment estimates
Not built to scale to very large student populations yet

## Slide 7
PART ONE
System Design & Architecture
How the three parts of SecureTap fit together, and the process each scanner follows at the gate.

## Slide 8
ARCHITECTURE
Three Independent, Cooperating Programs
SYSTEM DESIGN
08
entry-agent
Guard's PC — camera + NFC reader
Tkinter desktop app · zero ML dependencies
Captures frames & card taps only
backend
Django REST API + MySQL
Owns the database · runs ALL face recognition
and liveness computation · enforces roles
dashboard
Browser — admin / security / IT
React web app · live monitoring, user
management, reports
HTTP / JSON — polling-based, no WebSocket server needed
Only the backend touches machine learning or the database. The entry-agent and dashboard are thin clients — the gate PC only needs to capture and display, not run a model.
SYSTEM DESIGN
08

## Slide 9
PROCESS
Camera Scanner — Step by Step
SYSTEM DESIGN
09
1
Capture
Frame grabbed every 0.2s
2
Detect
Every face found in-frame
3
Quality Gate
Skip blur / edge-cropped
4
Liveness Check
Real face, or spoof?
5
Match
Compare vs. enrolled faces
6
Vote & Log
Confirm across frames
If a face fails the liveness check
Routed to spoof-vote tracking, not identity matching — flagged
as SPOOF SUSPECTED, distinct from a routine unmatched face.
If a match is ambiguous
Two close candidates, or a borderline score, opens a 10-second
"tap your card to confirm" tiebreak window instead of guessing.
Nothing is logged from one frame alone
A result needs to be the consistent answer across several recent
scans before it's written as a permanent record or triggers an alarm.

## Slide 10
PROCESS
Card Scanner — Step by Step
SYSTEM DESIGN
10
1
Tap / Type ID
HID card tap, or manual
ID entry fallback
2
Lookup
Match against enrolled
student/staff record
3
Tiebreak Check
Resolves a pending face
tiebreak, if one is open
4
Log & Display
Full profile card shown
for a visual cross-check
Success
Enrolled + active → full profile card, logged as a successful entry/exit.
Not Registered
No matching student/staff record for that card or ID.
Deactivated
Record exists but has been deactivated by an admin.

## Slide 11
PART TWO
Core Technical Contributions
The three ideas that make SecureTap more than a card reader with a camera bolted on.

## Slide 12
INNOVATION 01
Continuous 1:N Face Recognition
CORE CONTRIBUTIONS
12
Not a stop-and-pose kiosk — the camera watches the gate continuously, identifying every face in frame, every ~0.2 seconds.
512-D
ArcFace embedding
per face
~5 fps
Continuous scan
rate
buffalo_s
Lightweight CPU-only
model pack
How matching works
Face detected → 512-d embedding computed (InsightFace / ArcFace)
Compared via cosine similarity against every enrolled person's stored embeddings — one vectorized operation
Best match wins, if above FACE_MATCH_SIMILARITY_THRESHOLD
A person can enroll up to 5 embeddings (multiple angles) — best of the 5 counts

## Slide 13
INNOVATION 02
Passive Anti-Spoofing on a Standard Webcam
CORE CONTRIBUTIONS
13
No depth or infrared sensor is assumed — this had to work on the same 2D webcam already used for recognition. Two independent signals combine into one score.
PRIMARY · 65%
MiniFASNetV2
Trained CNN · Minivision AI · Apache-2.0
Classifies an 80×80 face crop as live / print-attack / replay-attack
Trained specifically on print & screen spoof data
From-source ONNX export — official weights hash-verified,
numerically matched to PyTorch (diff < 1.4×10⁻⁶)
SECONDARY · 35%
Classical CV Cues
Texture · Frequency · Reflectance analysis
Local Binary Patterns — real skin micro-texture vs. flat print/screen
2D FFT — catches halftone dot & screen moiré patterns
HSV reflectance — screens/glossy prints reflect light differently
than skin
Also serves as the automatic fallback if the trained model is ever unavailable — the check never hard-fails.

## Slide 14
INNOVATION 02
Verified Against Real Spoof Attempts
CORE CONTRIBUTIONS
14
Tested end-to-end — real face detection, the model's own crop convention, and the exported model — against labeled real & spoof sample photos.
REAL FACE
99.97%
correctly scored LIVE
SPOOF PHOTO #1
0.81%
correctly scored SPOOF
SPOOF PHOTO #2
0.07%
correctly scored SPOOF
Measured performance
~2.3 ms
per-face liveness scoring time (warm)
~400-900 ms
ArcFace inference already dominates each cycle
Net effect: liveness detection adds negligible latency to the gate scan.

## Slide 15
INNOVATION 03
Face + NFC — Complementary, Not Redundant
CORE CONTRIBUTIONS
15
The NFC card isn't a second copy of the same check — it resolves exactly the cases face recognition alone can't decide.
Clear match
Confirmed automatically
face_only
Ambiguous match
Card tap breaks the tie
(10s window)
face_and_card_tiebreak
No match
Logged as unrecognized,
photo captured
face_only (failed)
Suspected spoof
Flagged distinctly —
not a routine miss
spoof_suspected
Also stands alone
A plain NFC tap or manual ID entry works as an independent verification path too — for routine spot checks or whenever using the camera isn't practical.

## Slide 16
RELIABILITY
One Frame Is Never Enough
CORE CONTRIBUTIONS
16
Matches, non-matches, AND spoof suspicions all go through the same multi-frame majority vote before becoming a permanent record.
Frame 1
✓
Frame 2
?
Frame 3
✓
Frame 4
✓
3 of 4 agree
CONFIRMED
4
VOTE_WINDOW_SIZE
recent attempts considered
2
VOTE_REQUIRED_AGREEMENT
must agree to confirm
4s
VOTE_WINDOW_SECONDS
time window for those attempts
Result: one bad frame can't wrongly flag a real student as Unknown or as a spoof — and one lucky frame can't wrongly confirm a stranger.

## Slide 17
PART THREE
Platform, Privacy & Results
The admin experience, how the system protects data, and what we measured.

## Slide 18
PLATFORM
Admin Dashboard & Reporting
PLATFORM
18
Live Monitoring
Real-time photo-grid feed of today's gate activity with method/status badges and confidence.
Logs
Filterable, paginated history by date, name, gate, and status — with CSV export.
User Management
Guided 5-shot enrollment with live photo-quality checks, plus bulk CSV/XLSX import.
Reports
Entries by method, confidence histogram, busiest hours, and a preliminary FAR/FRR curve.

## Slide 19
TRUST
Data Privacy & Security
PLATFORM
19
Embeddings, not photos
Biometric matching is stored as 512-d vectors — not raw face images — specifically to reduce biometric exposure.
bcrypt + JWT
Dashboard passwords hashed with bcrypt; sessions use short-lived, rotated JWT tokens.
Verified model provenance
The liveness model is a from-source export with hash-verified weights and a documented chain of custody — not an unverified download.
RA 10173 — Data Privacy Act
Continuous scanning captures biometric data on everyone passing the gate — not just enrolled users. Real deployment requires:
Written consent collection
A visible notice at the gate
Data-use & retention disclosure
A correction/deletion request process
Data Protection Officer sign-off

## Slide 20
RESULTS
Actual Accomplishments
PLATFORM
20
Completed Modules
Entry-Agent App: Tkinter gate scanner with local SQLite queue for offline resilience.
Backend REST API: Django server handling face recognition & liveness detection models.
Admin Dashboard: React web app for real-time live monitoring, profiles, and reports.
MySQL Database: Centralized storage for enrolled persons, embeddings, and logs.
Secure Authentication: Dual token scheme (JWT for dashboard, service tokens for edge agents).
Key Accomplishments
Development Status: 100% Completed Core System
The system is fully developed, integrating face recognition (InsightFace/ArcFace) and passive liveness detection (MiniFASNetV2 + classical cues) with zero external dependencies on the edge gate PC. Major Features Operational: • Continuous 1:N Face Recognition (0.2s scan interval, ~5 fps) • Passive Anti-Spoofing (2.3ms latency, 2D webcam compatible) • Face + NFC Interplay (automated card-tap tiebreak resolved in 10s) • Multi-Frame Majority Voting (noise/error filtering for gate events)

## Slide 21
WRAPPING UP
Future Work & Conclusion
CONCLUSION
21
Future Work
Threshold tuning against real enrolled-population data
Vector-index search (FAISS) for large-scale enrollment
3D/silicone-mask-aware liveness signal
Multi-gate registry & per-gate configuration
Push notifications for flagged / spoof events
Conclusion
EVSU SecureTap shows that reliable, spoof-resistant biometric gate security doesn't require specialized depth or infrared hardware.
By combining continuous ArcFace recognition, a two-signal passive liveness check, and NFC as an intelligent tiebreaker — all confirmed through multi-frame voting — the system verifies identity, not just possession of a card, using only a standard webcam.

## Slide 22
Thank You
Questions & Discussion
EVSU SecureTap · Eastern Visayas State University